## Slide 1
Explorer Compressor Inhibit & RECIRC Override Analysis
Ford Confidential
Mahtab J Fard
April 15, 2020
Connected Vehicle Analytic – GDIA

## Slide 2: Background
Climate control team has been working on a Climate Quality Energy Room focused on reducing Warranty Spend. Compressor replacements is the #2 item for Climate. Within that category, there’s a significant number (35%) of returned compressors from warranty repairs that show no issue when they are analyzed (in particular on the pre-2020 Explorer). So they are trying to understand the underlying cause of the customer complaint of A/C slow to cool or does not work.

## Slide 3: AC System & Sensors
*Reference: https://carhowto.com/how-your-cars-ac-system-works/
Blower Speed
Evaporation Temperature
Clutch On/Off
Engine RPM
High Side Pressure
Fan Speed
Additional: Wiper Status, Ambient Air Temperature, Vehicle Acceleration, Vehicle Speed

## Slide 4: Big Data Drive (BDD) *:
Big Data Drive uses an Open XC plug-in device to record vehicle data.
The device is connected via the OBD II port and collects vehicle CAN data, which is then sent via Bluetooth to an onboard phone.
The phone then transmits the CAN data via WIFI (when the user connects while at home) or via cellular (select cases).
CAN messages are transmitted as encoded hexadecimal signals (ex. 0xcf390011030f0b0c) which then have to be decoded into human-readable values.
A DBC file encodes raw CAN vehicle data into a human-readable and standardized format. A vehicle may have multiple CAN buses (HS1/HS2/MS) and every CAN bus is represented by its own DBC file.
The image below shows the general structure of a DBC file - which is essentially a database format structured around messages and signals.
*Reference: https://github.ford.com/GDIA/ConnectedVehicleAnalytics/tree/master/BDD/decode

## Slide 5: Objectives
We developed the following objectives with hopes to further analyze this climate system challenge.
Identify selection criteria for F-150s.
Determine CAN signals of interest.
Collect data for F-150s.
Conduct analysis.
Scale study to other vehicle types.
Perform rudimentary analysis on Explorer.

## Slide 6: F-150 Selection Criteria
Ensure at least 30 days worth of recorded data transfers.
Preferable to select fewer vehicles with more frequent transfers, rather than more vehicles with less transfers and a shorter timestamp range.
Focus on 2018 & 2019 F-150.
Subset vehicles with transfer timestamps during summer months (May - August).
Select vehicles with variable displacement compressors.
784 F-150 VINs from BDD
64 2018 F-150s
100 2019 F-150s

## Slide 7: F-150 Selection
Extract all 784 F-150 VINs from BDD.

## Slide 8: F-150 Selection
64 2018 F-150s subset based on selection criteria.

## Slide 9: F-150 Selection
100 2019 F-150s subset based on selection criteria.

## Slide 10: Understanding the Difference in Actual and Requested Temperature

## Slide 11: Understanding the Difference in Actual and Requested Temperature

## Slide 12: Understanding the Difference in Actual and Requested Temperature

## Slide 13: Understanding the Difference in Actual and Requested Temperature

## Slide 14
Demo

## Slide 15: Analyzing Time Intervals With Negative Temperatures

## Slide 16: Analyzing Time Intervals With Negative Temperatures
Over the span of summer 2019 (May - July), the actual temperature is below 0°C every 161296 seconds (1.8 days) on average.

## Slide 17: Analyzing Time Intervals With Negative Temperatures

## Slide 18: Analyzing Time Intervals With Negative Temperatures

## Slide 19: Analyzing Time Intervals With Negative Temperatures
Interval 57 looks particularly concerning, as it lasts the longest (31 seconds) and reaches a minimum temperature of -0.6.

## Slide 20: What’s Next?
Identify selection criteria for F-150s.
Determine CAN signals of interest.
Collect data for F-150s.
Conduct analysis.
Scale study to other vehicle types.
Perform rudimentary analysis on Explorer.